## Slide 1: C Programming
Chapter 4

## Slide 2: C Relational operators
A relational operator checks the relationship between two operands. If the relation is true, it returns 1; if the relation is false, it returns value 0.
Relational operators are used in decision making and loops.

## Slide 3
Operator | Meaning of Operator | Example
== | Equal to | 5 == 3 is evaluated to 0
> | Greater than | 5 > 3 is evaluated to 1
< | Less than | 5 < 3 is evaluated to 0
!= | Not equal to | 5 != 3 is evaluated to 1
>= | Greater than or equal to | 5 >= 3 is evaluated to 1
<= | Less than or equal to | 5 <= 3 is evaluated to 0

## Slide 4: Practice with Relational Expressions
int a = 1, b = 2, c = 3 ;
Expression Value Expression Value
a < c a + b >= c
b <= c a + b == c
c <= a a != b
a > b a + b != c
b >= c
T
T
F
F
F
T
T
T
F

## Slide 5: C Logical Operators
An expression containing logical operator returns either 0 or 1 depending upon whether expression results true or false.
Logical operators are commonly used in decision making in C programming.

## Slide 6: C Logical Operators contd…
Sometimes we need to test multiple conditions in order to make a decision.
Logical operators are used for combining simple conditions to make complex conditions.

## Slide 7
Operator | Meaning of Operator | Example
&& | Logical AND. True only if all operands are true | If c = 5 and d = 2 then, expression ((c==5) && (d>5)) equals to 0.
¦¦ | Logical OR. True only if either one operand is true | If c = 5 and d = 2 then, expression ((c==5) ¦¦ (d>5)) equals to 1.
! | Logical NOT. True only if the operand is 0 | If c = 5 then, expression !(c==5) equals to 0.

## Slide 8: Practice question
Given
int a = 5, b = 7, c = 17 ;
evaluate each expression as True or False.
1. c / b == 2
2. c % b <= a % b
3. b + c / a != c - a
4. (b < c) && (c == 7)
5. (c + 1 - b == 0) || (b = 5)

## Slide 9: Bitwise operators in C
In arithmetic-logic unit (which is within the CPU), mathematical operations like: addition, subtraction, multiplication and division are done in bit-level.
To perform bit-level operations in C programming, bitwise operators are used.

## Slide 10
Operator | Meaning of Operator
& | Bitwise AND
¦ | Bitwise OR
^ | Bitwise XOR
~ | Bitwise complement
<< | Shift left
>> | Shift right

## Slide 11: Bitwise AND
The output of bitwise AND is 1 if the corresponding bits of two operands is 1. If either bit of an operand is 0, the result of corresponding bit is evaluated to 0.

## Slide 12: Bitwise AND
12 = 00001100 (In Binary)
25 = 00011001 (In Binary)
Bit Operation of 12 and 25
00001100
& 00011001
________
00001000 = 8 (In decimal)

## Slide 13: Bitwise AND example
#include <stdio.h>
int main()
{
int a = 12, b = 25;
printf("Output = %d", a&b);
return 0;
}
//output 8

## Slide 14: Bitwise OR
The output of bitwise OR is 1 if at least one corresponding bit of two operands is 1.
In C Programming, bitwise OR operator is denoted by |.

## Slide 15: Bitwise OR
12 = 00001100 (In Binary)
25 = 00011001 (In Binary)
Bit Operation of 12 and 25
00001100
& 00011001
________
00011101 = 29 (In decimal)

## Slide 16: Bitwise OR example
#include <stdio.h>
int main()
{
int a = 12, b = 25;
printf("Output = %d", a|b);
return 0;
}
//output 29

## Slide 17: Bitwise XOR (exclusive OR) operator ^
The result of bitwise XOR operator is 1 if the corresponding bits of two operands are opposite.
It is denoted by ^.

## Slide 18: Bitwise XOR (exclusive OR) operator ^
12 = 00001100 (In Binary)
25 = 00011001 (In Binary)
Bitwise XOR Operation of 12 and 25
00001100
^ 00011001
________
00010101 = 21 (In decimal)

## Slide 19: Example: Bitwise XOR
#include <stdio.h>
int main()
{
int a = 12, b = 25;
printf("Output = %d", a^b);
return 0;
}
//output 21

## Slide 20: Bitwise complement operator
Bitwise compliment operator is an unary operator (works on only one operand).
It changes 1 to 0 and 0 to 1. It is denoted by ~.

## Slide 21: Bitwise complement operator
35 = 00100011 (In Binary)
Bitwise complement Operation of 35
~ 00100011
________
11011100 = 220 (In decimal)

## Slide 22: Bitwise complement operator
35 = 00100011 (In Binary)
Bitwise complement Operation of 35
~ 00100011
________
11011100 = 220 (In decimal)

## Slide 23: Bitwise complement operator
The bitwise complement of 35 (~35) is -36 instead of 220, but why?
For any integer n, bitwise complement of n will be -(n+1).
To understand this, you should have the knowledge of 2's complement.

## Slide 24: 2's Complement
The 2's complement of a number is equal to the complement of that number plus 1. For example:
Decimal: 220 Binary: 11011100 -(00100011+1) [-(n+1)]
= -00100100
= -36(decimal)

## Slide 25: Bitwise complement operator
The bitwise complement of 35 is 220 (in decimal). The 2's complement of 220 is -36. Hence, the output is -36 instead of 220.

## Slide 26: Example bitwise complement
#include <stdio.h>
int main()
{
int a=35,b=-12;
printf("Output = %d\n",~a);
printf("Output = %d\n",~b);
return 0;
}//output -36,11

## Slide 27: Shift operators in C
There are two shift operators in C programming:
  Right shift operator
  Left shift operator.

## Slide 28: Right Shift Operator
Right shift operator shifts all bits towards right by certain number of specified bits.
It is denoted by >>.

## Slide 29: Right shift operator
220 11011100 (220)
220 >> 2 00110111 (55)

## Slide 30: Example right shift operator
#include <stdio.h>
int main()
{
int num=220;
printf("right shift 220 by 2 bits %d",num>>2);
return 0;
}

## Slide 31: Left shift operator
Left shift operator shifts all bits towards left by a certain number of specified bits.
The bit positions that have been vacated by the left shift operator are filled with 0.
The symbol of the left shift operator is <<.

## Slide 32: Left shift operator
220 11011100 (220)
220 << 2 11011100 00 (880)

## Slide 33: Example left shift operator
#include <stdio.h>
int main()
{
int num=220;
printf("right shift 220 by 2 bits %d",num<<2);
return 0;
}//output 880

## Slide 34: Comma as an operator
Sometimes we assign multiple values to a variable using comma, in that case comma is known as operator.
Example:
a = 10,20,30;
In the above statement, value of a will be 10, because assignment operator (=) has more priority more than comma (,), thus 10 will be assigned to the variable a.

## Slide 35: Comma as an operator
Sometimes we assign multiple values to a variable using comma, in that case comma is known as operator.
Example:
b = (10,20,30);
In the second statement, value of b will be 30, because 10, 20, 30 are enclosed in braces, and braces has more priority than assignment (=) operator. When multiple values are given with comma operator within the braces, then right most value is considered as result of the expression. Thus, 30 will be assigned to the variable b.

## Slide 36: Comma as an operator
#include <stdio.h>
int main()
{
int a,b;
a = 10,20,30;
b = (10,20,30);
//printing the values
printf("a= %d, b= %d\n",a,b);
return 0;
}

## Slide 37: Comma as a separator
Comma acts as a separator when used with function calls and definitions, function like macros, variable declarations, enum declarations, and similar constructs.
Example
  int a = 1, b = 2;
  void fun(x, y);

## Slide 38: Conditional Operator in C
The conditional operator is also known as a ternary operator. The conditional statements are the decision-making statements which depends upon the output of the expression.
It is represented by two symbols, i.e., '?' and ':'.
The behavior of the conditional operator is similar to the 'if-else' statement.

## Slide 39: Syntax: conditional operator
Syntax of a conditional operator
  Expression1? expression2: expression3;
  (condition ? value_if_true : value_if_false)

## Slide 40: Syntax: conditional operator

## Slide 41: Example conditional operator
#include <stdio.h>
int main()
{
int a = 10, b = 20, c;
c = (a < b) ? a : b;
printf(“c = %d", c);
return 0;
}

## Slide 42: Nested conditional operator
#include <stdio.h>
int main()
{
float unit_price = 10.0, dis1 = 0.05, dis2 = 0.1, dis3 = 0.15, total_price;
int qty = 11;
total_price = qty*unit_price*(1.0 -
(qty>50 ? dis1 : (
qty>20 ? dis2 : (
qty>10 ? dis3 : 0.0))));
printf("The total price is %.2f\n", total_price);
return 0;
}

## Slide 43: Conditional (ternary) operator
As we know that the behavior of conditional operator and 'if-else' is similar but they have some differences. Let's look at their differences.
Conditional operator is a single statement where if-else comes in a block.
We can use conditional operator to assign values to a variable whereas it is not possible in if-else
Not useful for executing multiple statements, whereas it is easy in if-else.
Nested ternary operator is more complex and cannot be easily debugged, while the nested 'if-else' statement is easy to read and maintain.

## Slide 44: Type casting
Type casting refers to changing an variable of one data type into another.
  Implicit type casting
  Explicit type casting

## Slide 45: Implicit Type Conversion
When the type conversion is performed automatically by the compiler without programmers intervention, such type of conversion is known as implicit type conversion or type promotion.

## Slide 46: Example Implicit Type Conversion
#include<stdio.h>
int main(){
int x=97;
printf("%c", x);
/*Implicit casting from int to char */
return 0;
}// output a

## Slide 47: Explicit Type Conversion
The type conversion performed by the programmer by posing the data type of the expression of specific type is known as explicit type conversion. The explicit type conversion is also known as type casting.

## Slide 48: Explicit Type Conversion
Type casting in c is done in the following form:
  (data_type)expression;

## Slide 49: Example explicit type conversion
int x=7, y=5;
float z;
z = (float)x/(float)y;
/*Here the value of z is 1.4*/